## Slide 1: Electrical Engineer Co-op Presentation Northwood E&I
David Emelu
UVIC – 2nd Year Electrical Engineering
January 2024 – August 2024
Supervisors: Savio D’Silva, Denni Thompson and Ryan Swanson
Manager: Umunna Uwom

## Slide 2: Outline
Supplementary
Project Involvements
Project Descriptions
Methodology
Results
Benefit to the mill
Workshops

## Slide 3: Projects
MCC/MCC Room Drawing Audits
‘A’ Digestor Provox Migration Project
Distribution and Precipitator Transformer Summary Report
B Diffuser Hydraulic bypass using Local Selector Switch Installation and PLC Rewiring
VFD migration for B Bleach 50% Peroxide Pump and R8 93% H2S04 Generator

## Slide 4: MCC/MCC Room Drawing Audits
Audit MCC/MCC Room layout
Update asset list in each MCC/MCC Room
Identify undocumented power cross-feed and create a cable block diagram
Scope of work

## Slide 5: MCC/MCC Room Drawing Audits - Methodology
1
Assembled a binder containing all MCC/MCC room layouts drawings for easy reference.
2
Conducted thorough field checks to identify discrepancies and verify asset statuses.
3
Evaluated changes and prepared revised drawings for drafting..
4
Mapped existing power cross-ties on a cable block diagram to identify cross-feed locations for emergency power.

## Slide 6: MCC/MCC Room Drawing Audits
‘A’ KILN MCC ROOM AUDIT

## Slide 7: CROSS FEED
Fiber line area
Steam plant area

## Slide 8: CROSS FEED
Importance of documenting power cross-feeds locations
Safety: Without proper documentation, it is easy to make mistakes during maintenance or emergency situations, which can lead to accidents or equipment damage
Lockout Planning: Documenting cross-feed locations help in knowing the exact power sources and connections which helps in isolating specific equipment safely, reducing the risk of electrical hazards during maintenance.

## Slide 9: VFD migration (From Mitsubishi A560 – A860)
Scope of work
Procure replacement VFD, option cards and pull-down resistor pack for 22-2624 and 26-1213.
Mark up the conversion package (A560 to A860) drawing using the wiring and schematic diagram of the existing drawing.
Remove Mitsubishi a560 from service and Install a860 in service

## Slide 10: VFD migration (From Mitsubishi A560 – A860)
MARKED UP WIRING AND BLOCK DIAGRAM FOR POWER AND AC CONTROL FOR THE VFDs
22-2624: R8 93% H2S04
23-1213: B BLEACH 50% PEROXIDE

## Slide 11: VFD migration – Results
OLD VFD SETUP
NEW VFD SETUP
OLD VFD SETUP
NEW VFD SETUP
R8 93% H2S04 PUMP VFD UPGRADE
B BLEACH 50% PEROXIDE PUMP VFD UPGRADE

## Slide 12: ‘A’ Digestor Provox Migration Project
Rack Drawing Creation: Audit the marshaling racks with an instrument mechanic to collect conductor and cable tag information and create a rack drawing for Rack 18A and 18B, which has not been previously made.
I/O Points Audit: Input loop details into an Excel spreadsheet to create a master I/O list for loops in file 2 and cross-check the information with the drawing of each loop.
Mapping I/O and Updating Loop Sheets: Map old Provox I/O points to new points on the Delta V controller, and ensuring all new terminations are accurately updated and documented across over 100 instrumentation loop drawings related to File 2.
Scope of work

## Slide 13: ‘A’ Digestor Provox Migration Project
1
Visit the field with an instrument mechanic to collect information from the marshaling racks and create a comprehensive list for Rack 18A and 18B.
2
Document I/O List in a spreadsheet
4
Map old Provox I/O points in file 2 to new points on the Delta V controller,

## Slide 14: ‘A’ Digestor Provox Migration Project

## Slide 15: ‘A’ Digestor Provox Migration Project

## Slide 16: ‘A’ Digestor Provox Migration Project
Provox controller (File 2)
Delta V M-Series Controller

## Slide 17: Benefits to the mill
MCC/MCC Room Drawing Audits
Improved Emergency Preparedness
A-DIG Migration Project
Upgrading Obsolete asset
More stable operation
Distribution and Precipitator Transformer Summary Report
VFD migration for B Bleach 50% Peroxide Pump and R8 93% H2S04 Generator
Enhanced Maintenance Coordination
Proactive Maintenance Planning
Upgrade from Obsolete model
Cost Savings and Risk Management

## Slide 18: Supplementary – Workshops
Learning PLC Basics
Learning to basics of wiring a relay
Delta-V and AMS Training

## Slide 19: THANK YOU!!